## Slide 1: RA 505 Robot Sensing and Vision Lecture 24
Dr. Rishikesh Kulkarni
Department of Electronics and Electrical Engineering
IIT Guwahati

## Slide 2: Fourier transform

## Slide 3: DIGITAL STILL CAMERA
Imaging optics, imaging elements, and image-processing technology
Schematic diagram of single lens
Refractive power/ power of lens = inverse of the focal length
retrofocus type
telephoto type

## Slide 4: DIGITAL STILL CAMERA
effective F-number
brightness of the lens (the image plane brightness) ∝ 1/F2
When the distance to the object is limited, the image
is formed farther away from the lens than is the case for very far-off objects, so the brightness at the image plane (the surface of the imaging element) is lower.

## Slide 5: DIGITAL STILL CAMERA
This equation gives us the brightness at the centre of the image, but the brightness at the periphery of the image is generally lower than this.
The cosine fourth law: theta is the angle diverging from the optical axis facing towards the photographed area on the object side (half the field of view).
‘Wide-angle lens’: field of view of 65 degree or more
‘Telephoto lens’: field of view of 25 degree or less
Modulation transfer function (MTF) and resolution: Frequently used as a standard for evaluating the imaging performance of any lens
Higher the frequency (the more detailed the object pattern), the greater the decline in object reproducibility.
Resolution: measure for evaluating the level of detail that can be captured; line-pairs/mm