## Slide 1: RA 505 Robot Sensing and Vision Lecture 22
Dr. Rishikesh Kulkarni
Department of Electronics and Electrical Engineering
IIT Guwahati

## Slide 2: Syllabus
Binary, monochrome and RGB imaging sensors
Velocity sensors,
Accelerometers
Tactile sensors.
Ultrasound rangefinders
Optical rangefinders - LASER scanner, static LED array
Structured lighting, dynamic focusing
Interfacing of vision sensors

## Slide 3: DIGITAL CAMERA
Difference between a silver halide photographic camera and an electronic still camera
Conventional silver halide cameras
Electronic still cameras
  Analog storage
  Digital storage
Mavica (Magnetic video camera)
  image signals captured by the semiconductor image sensor
  stored on a magnetic floppy disk.
Why did still video system fail?
  Cost
  Poor picture print quality (VGA quality (640 × 480 pixels))

## Slide 4: DIGITAL CAMERA
Fuji digital still camera DS-1P (CCD+Static RAM)
Kodak DCS-1
Casio QV-10 (LCD monitor display)

## Slide 5: DIGITAL CAMERA
Typical arrangement of an SLR digital still camera
Typical block diagram of a digital still camera.
Additional optics (IR filter + Optical LPF)

## Slide 6: DIGITAL CAMERA
OPTICS
  Objective lens, IR filter, optical low pass filter
IMAGING DEVICES
  CCD and CMOS sensors
ANALOG CIRCUIT
  Sample-and-hold, color separation, AGC (automatic gain control), level clamp, tone adjustment, ADC
DIGITAL CIRCUIT
  DSP; tone adjustment; RGB to YCC color conversion; white balance; image compression/decompression; exposure control, auto focus, and automatic white balance
SYSTEM CONTROL
  exposure control (AE), auto focus

## Slide 7: References
Image sensors and Signal Processing for Digital Still Cameras, Ed. Junichi Nakamura, Taylor & Francis Group, LLC, 2006.