## Slide 1: RA 505 Robot Sensing and Vision Lecture 27
Dr. Rishikesh Kulkarni
Department of Electronics and Electrical Engineering
IIT Guwahati

## Slide 2: Photodetector in a pixel
Microlens array
  On-chip microlens array(OMA)
  Collimates light to the photodiode
  color filter layer-> transparent resin
  photolithographic patterning
  Increase in sensitivity
  Shading effect
  Reduce smear in CCD image sensors and crosstalk between pixels caused by minority carrier diffusion
Reflection at SiO2 and Si interface
  Refractive index variation causes reflection
  more than 20 to 30% of the incident light is reflected at the silicon surface in the visible light range
  Anti-reflective films formed above the photodiode

## Slide 4: Photodetector in a pixel
Charge collection efficiency
  Depends on substrate type, impurity profile, minority carrier lifetime in the bulk and photodiode biasing
Full-well capacity
  photodiode operates in the charge-integrating mode
  Limited charge handling capacity
  Saturation charge

## Slide 5: Noise
Fixed pattern Noise (FPN) vs Random/Temporal noise
FPN at dark: dark signal non-uniformity (DSNU)
FPN at illumination: photo-response nonuniformity (PRNU)
Exposure variation: sensitivity nonuniformity or gain variation
FPN sources: long exposure times /high temperatures (CCD), dark current nonuniformity and performance variations of an active transistor inside a pixel (CMOS)
Dark current
  reduces the imager’s useable dynamic range
  Generation Current in the Depletion Region
  Surface Generation
  Diffusion current
  Temperature Dependence

## Slide 6: Noise
Shading
  slowly varying or low spatial frequency output variation
  Dark-current-oriented, Microlens-oriented, Electrical-oriented shading
Temporal noise
  random variation in the signal over time
  Probability distribution
  Thermal noise
    thermal agitation of electrons
  Shot noise
    arises because of the discrete nature of the charges carried by charge carriers
  Power spectral densities of thermal noise and shot noise are constant over all frequencies.
  1/f noise: correlated double sampling
  Read noise/noise floor
Smear: white vertical stripes
Blooming: photogenerated charge exceeds a pixel’s full-well capacity
Image lag

## Slide 8: Photoconversion characteristics
Quantum efficiency
Responsivity
Dynamic range:
Signal to noise ratio

## Slide 9: Photoconversion characteristics
Estimation of quantum efficiency