## Slide 1: RA 505 Robot Sensing and Vision Lecture 32
Dr. Rishikesh Kulkarni
Department of Electronics and Electrical Engineering
IIT Guwahati

## Slide 2: Velocity sensors
Optical, capacitive or magnetic
potentiometer as a velocity transducer
  require interfacing to a differentiator circuit
  difficult to stabilize
  use is not recommended
Tachogenerator
  Dual of electric motor
  DC type (dynamo)
  AC type (alternator)
  Need no power supply
  Analog output, requires ADC

## Slide 3: Interfacing of Velocity sensors
Tachogenerator
Optical Encoder
Low voltage pulse train
frequency is proportional to angular speed
Counting number of lined detected by photo-diode in unit time
Time taken by the photo-diode to detect a single line

## Slide 4: Tactile sensors
Tactile sensing allows continuous measurement of the pressure distribution across an array of so called ‘tactels’
detection of slippage
Inspection

## Slide 5: Resistive Tactile sensors
Most popular
higher sensitivity and x-y resolution
carbon fibres, conductive rubbers, media impregnated with conductive dopants (lower hysteresis and larger dynamic range)
Change in resistance in function of pressure
Capacitive effect

## Slide 6: Capacitive Tactile Sensors
potential for measuring higher pressures
inherently less malleable
more mechanically robust
bigger tactel size
lower x-y tactel resolution

## Slide 7: Optical Tactile Sensors
changing the light absorption characteristics of the transparent medium under the effect of an applied force
plastics and glass fibres
used within a robot multisensory feedback system

## Slide 8: Resistance Strain Gauge
Highly popular passive type transducers
stress (force/unit area) and strain (elongation or compression/unit length) is developed on a object due to applied pressure
strain is used as an index of pressure
If a metal is compressed or stretched, its resistance changes on account of changes in its dimensions, i.e., length and cross-sectional area
Types
  Wire strain gauges
  Foil strain gauges
  Semiconductor strain gauges

## Slide 9: Resistance Strain Gauge
Wire strain gauges
  unbounded resistance wire strain gauges
  Bonded resistance wire strain gauges.
    Fine wire: about 25 um or less
    Carrier: thin sheet of paper.
    the carrier mounting of wire structure and carrier adhesion on the object surface plays a crucial role in strain measurement accuracy

## Slide 10: Resistance Strain Gauge
Resistance of a conductor
change in resistance due to the change in dimension and change is fundamental property of the material (piezoresistance)
Strain
Poisson ratio:

## Slide 11: Resistance Strain Gauge
Unbounded metal-wire gage
Bonded metal-wire gage
Bonded metal-foil gage
Vacuum-deposited thin-metal-film gage
Sputter-deposited thin-metal-film gage
Bonded semiconductor gage
Diffused semiconductor gage

## Slide 12: Resistance Strain Gauge
Bonded metal foil strain gauges
  Copper-Nickel, Nickel-Iron alloys;
  Thin metal grid mounted on flexible or brittle carrier;
  measurement of average strain over an area;
  Types of gauges are: Grid, Rossette, Torque and Helical.
  The area is comparatively more than the wire strain
  The resistive film thickness is typically 0.2mm thick.
  120 Ω, 350 Ω, 1000 Ω

## Slide 13: Resistance Strain Gauge
Rosette are nothing but three strain gauges overlapping at a same point manufactured on the same carrier material.
Rosettes are used for the measurement of force, velocity, pressure and displacement in applications such as aircraft and missile production, mechanical engineering, railroad, car manufacturing and other industries.

## Slide 14: Resistance Strain Gauge

## Slide 15: Resistance Strain Gauge