## Slide 1: RA 505 Robot Sensing and Vision Lecture 34
Dr. Rishikesh Kulkarni
Department of Electronics and Electrical Engineering
IIT Guwahati

## Slide 2: Accelerometer
Device to measure
  Acceleration
  Vibration
  Shock
  Velocity
  Position
Applications in
  Automotive
  Medical
  Industrial control
  Robotics
Types
  Hall effect
  Piezoelectric
  Piezoresistive
  Capacitive
  Position

## Slide 3: Hall effect based Accelerometer
Output signal from a Hall effect accelerometer is the function of magnetic field density around the device
Hall Effect Sensors
  A thin piece of rectangular p-type semiconductor material
  Gallium arsenide (GaAs), indium antimonide (InSb) or indium arsenide (InAs)
  A continuous current is passed through it
  Magnetic force (Lorenz force) experienced by charge carrier displaces them
  Hall voltage (VH)
  Built-in DC amplifiers, logic switching circuits and voltage regulators
  Bipolar/unipolar

## Slide 4: Hall effect based Accelerometer
Types of magnet movements, such as “Head-on”, “Sideways”, “Push-pull” or “Push-push” etc. sensing movements.
Useful in environmental conditions consisting of water, vibration, dirt or oil

## Slide 5: Piezoresistive Accelerometer
can measure both dynamic and static accelerations.
Gauge dimension, gauge factor, power dissipation
Creep: nonideal elastic behaviors of piezoresistors and adhesive materials
Temperature coefficient of resistance (TCR)
Temperature coefficient of sensitivity (TCSR),

## Slide 6: Capacitive Accelerometer
Spring-mass system
Change in capacitance due to change in distance between movable and fixed plate

## Slide 7: Piezoelectric Accelerometer
Piezoelectric material slice: Polarized ceramic
Advantages
  Frequency response
  Temperature stability
  Ruggedness
  Adaptability
  Electrical characteristics

## Slide 8: Potentiometric Accelerometer